## Slide 1
HACKTRONICS 2ND EDITION
FIREGUARD
Computational Threat-Zone Estimation
for Industrial Fire & Explosion Response
TEAM ATOM · TEAM NO. 38
SANTHOSH V — 24BPS1112
DAKSHA BORDEKAR — 24BRS1296
PRANAV SHINDE — 24BAI1590

## Slide 2
"A Fire Is Not a Circle."
CONVENTIONAL APPROACH
TANK
⭕ Fixed Radius Circle
✗ Source characteristics
✗ Tank geometry & volume
✗ Thermal radiation physics
✗ Blast overpressure model
✗ Wind conditions
✗ Spatial variation
FIREGUARD APPROACH
WIND
EXTREME
HIGH
MODERATE
🌐 Physics-derived spatial hazard field
"The challenge is not drawing a boundary. The challenge is computing where the consequence becomes dangerous."

## Slide 3
"From Incident Parameters to a Spatial Consequence Field"
FACILITY
Location · Tank Geometry · Volume
MATERIAL
Physical Properties
SCENARIO
Fire / Explosion Conditions
ENVIRONMENT
Wind Speed · Wind Direction
SOURCE CHARACTERIZATION
Energy Release · Geometry
THERMAL RADIATION
Point source · View factor
Radiative flux · Attenuation
BLAST OVERPRESSURE
TNT-equiv. · Scaled distance
Peak overpressure · Impulse
POINT CONSEQUENCE EVALUATION
Max(thermal, blast) per grid point
SPATIAL GRID
Structured evaluation over surrounding area
HAZARD FIELD
Consequence intensity at every location
SEVERITY CLASSIFICATION
EXTREME / HIGH / MODERATE bands
APPROACH DIRECTION ANALYSIS
Sector exposure ranking
RESPONDER DECISION SUPPORT
Lower-exposure approach intelligence

## Slide 4
"The Physics Behind the Map"
THERMAL RADIATION MODEL
Fire Source
Tank fire scenario
Flame Characterization
Flame geometry · effective emissive power (EEP)
Geometric View Factor (F)
Solid angle subtended at receiver
Radiative Transfer
Atmospheric transmissivity (τ)
Receiver Point
Distance r from source
THERMAL FLUX q″ [kW/m²]
q″ = EEP × F × τ
Severity thresholds (kW/m²):
> 37.5 EXTREME — Fatal exposure
> 12.5 HIGH — Significant injury
> 4.7 MODERATE — Pain threshold
≤ 4.7 LOW — Acceptable for egress
BLAST OVERPRESSURE MODEL
Explosion Source
Tank explosion scenario
Energy Characterization
TNT-equivalent mass (W_TNT) from heat of combustion
Scaled Distance (Z)
Z = R / W_TNT^(1/3) — Hopkinson-Cranz scaling
Baker-Strehlow Model
Empirical overpressure vs. scaled distance
Receiver Point
Distance R from explosion centre
PEAK OVERPRESSURE ΔP [kPa]
Z = R / W^(1/3) → ΔP = f(Z)
Severity thresholds (kPa):
> 83 EXTREME — Severe structural damage
> 21 HIGH — Serious injury
> 6.9 MODERATE — Threshold injury
≤ 6.9 LOW — Minor effects
Two different physical quantities. Two independent consequence models. One spatial decision layer.

## Slide 5
"Every Point Becomes a Consequence"
Thousands of spatial evaluations → continuous hazard field
TANK
STRUCTURED SPATIAL GRID — Each node = one consequence evaluation
WIND →
TANK
EXTREME
HIGH
MODERATE
LOW
COMPUTED HAZARD FIELD — Physics-derived contours
Distance
Thermal q″
Blast ΔP
Severity
"We do not draw a predefined circle. The geometry emerges from spatial consequence calculations."

## Slide 6
"The Hazard Changes When the Scenario Changes"
WIND-DEPENDENT SPATIAL BEHAVIOR
WIND →
TANK
Upwind: reduced extent
Downwind: extended plume
MULTI-HAZARD SEVERITY BANDS
EXTREME
Thermal > 37.5 kW/m² · Blast > 83 kPa
HIGH
Thermal > 12.5 kW/m² · Blast > 21 kPa
MODERATE
Thermal > 4.7 kW/m² · Blast > 6.9 kPa
LOW
Thermal ≤ 4.7 kW/m² · Blast ≤ 6.9 kPa
SCENARIO COMPARISON
SCENARIO A
Small tank · Low wind · Pool fire
SCENARIO B
Large tank · High wind · BLEVE explosion
VS
Different physical inputs → Different computed consequences → Different hazard geometry

## Slide 7
"From Hazard Map to Approach Intelligence"
TANK
N HIGH
NE HIGH
E EXTREME
SE HIGH
S MODERATE
SW LOW ★
W LOW
NW MODERATE
WIND →
HAZARD
FIELD
DIRECTIONAL
ANALYSIS
RANK
SECTORS
LOWER-EXPOSURE
APPROACH
★ LOWER MODELED
EXPOSURE (SW)
⚠ If all directions exceed defined criteria → NO SAFE APPROACH IDENTIFIED
Screening-level decision support — not a certified safety boundary.

## Slide 8
"Why FIREGUARD?"
01
PHYSICS-BASED
Deterministic consequence models rather than arbitrary fixed circles.
02
SPATIALLY EXPLICIT
Evaluates consequences across the full surrounding area.
03
WIND-AWARE
Represents wind influence on hazard geometry.
04
MULTI-HAZARD
Thermal radiation + blast overpressure — two independent models.
05
DECISION-ORIENTED
Transforms hazard calculations into approach-direction intelligence.
06
EXPLAINABLE
Inputs → Models → Spatial field → Severity → Decision.
INCIDENT
PHYSICS
HAZARD FIELD
APPROACH INTELLIGENCE
"DON'T DRAW THE DANGER.
COMPUTE IT."
FIREGUARD · TEAM ATOM · HACKTRONICS 2ND EDITION